## Slide 1
Soil Moisture Prediction Using Machine Learning
An End-to-End Regression Approach Using Sentinel-1 SAR and SMAP Data Vassar Labs IT Solutions – Data Science Evaluation
Sachin Dimri
Machine Learning Project
February 12, 2026
Indian Institute of Technology Bombay

## Slide 2
Presentation Outline
Introduction & Problem Statement
Dataset Overview
Data Preprocessing & EDA
Model Development & Evaluation

## Slide 3
Introduction & Background
Soil moisture is critical for agriculture and climate monitoring
Traditional ground sensors are expensive and limited in coverage
Satellite remote sensing offers cost-effective large-scale monitoring
Machine learning can translate radar signals into moisture estimates

## Slide 4
Problem Statement
How can machine learning predict soil moisture from satellite radar backscatter data?
Sentinel-1 provides radar backscatter (VV, VH polarizations)
SMAP provides direct moisture measurements
Challenge: Complex non-linear relationships

## Slide 5
Project Objectives
Develop end-to-end ML pipeline for soil moisture prediction
Compare multiple regression algorithms systematically
Evaluate using RMSE, MAE, and R² metrics
Validate assumptions and interpret model limitations

## Slide 6
Dataset Overview
Total Observations: 30,747 records
Features: VV, VH (radar backscatter in dB), smapam (SMAP moisture)
Target: soil_moisture (volumetric content 0-1)
Data Quality: No missing values, 5 extreme outliers removed

## Slide 7
Data Sources
Sentinel-1 SAR
C-band radar at 5.4 GHz, 10-20m resolution, all-weather operation
SMAP Satellite
L-band radiometer, 36 km resolution, direct moisture sensing

## Slide 8
Data Preprocessing
Outlier Detection: 5 extreme values (>1000) removed from target
Train-Test Split: 80-20 ratio (24,593 train / 6,149 test)
Feature Scaling: Standardization (zero mean, unit variance)
Final Dataset: 30,742 observations ready for modeling

## Slide 9
Distribution Analysis - Key Findings
VV & VH: Approximately normal distributions (mean: -9.2, -16.4 dB)
smapam: Right-skewed with 19% zero values
soil_moisture: Right-skewed (mean: 0.174, std: 0.109)

## Slide 10
Correlation Analysis - Critical Finding
VV-VH Correlation: 0.888 (severe multicollinearity)
Predictor-Target Correlations: -0.065 to 0.041 (extremely weak)
Implication: Limited linear predictive signal

## Slide 11
Variance Inflation Factor (VIF)
VV VIF: 40.5 (severe multicollinearity)
VH VIF: 42.2 (severe multicollinearity)
smapam VIF: 2.2 (acceptable)
Action Taken: Tested model with VH removed (no improvement)

## Slide 12
Machine Learning Models - Part 1
Linear Regression (baseline model)
Polynomial Regression (degree 2)
Ridge Regression (L2 regularization)
Random Forest (ensemble of decision trees)

## Slide 13
Machine Learning Models - Part 2
Gradient Boosting (sequential tree learning)
Support Vector Regression - Linear Kernel
Support Vector Regression - RBF Kernel
Deep Neural Network (3 hidden layers)

## Slide 14
Performance Comparison
Best Model: Neural Network (R² = 0.056)
Second Best: SVR-RBF (R² = 0.053)
Worst: Random Forest (R² = 0.004)
RMSE Range: 0.106 - 0.109 (≈ target std dev)

## Slide 15
Linear Regression - Baseline
R² Score: 0.010 (1% variance explained)
RMSE: 0.109 (equal to target std dev)
MAE: 0.090
Interpretation: Model barely improves over mean prediction

## Slide 16
Linear Regression Assumptions
Linearity: ✓ Residuals randomly scattered
Normality: Slight violation (right skew)
Homoscedasticity: ✓ Variance reasonably constant
Multicollinearity: ✗ Severe (VIF > 40)

## Slide 17
SVR with RBF Kernel
Test R²: 0.053 (5.3% variance explained)
Cross-Val R²: 0.013 (stable generalization)
RMSE: 0.106 (slight improvement)
Strength: Captures non-linear patterns

## Slide 18
Deep Neural Network - Highest R²
Architecture: 64-32-16 neurons (ReLU activation)
Test R²: 0.056 (highest among all models)
RMSE: 0.106
Training: No overfitting observed

## Slide 19
Discussion - Key Findings
Consistent poor performance across all algorithms (R² < 0.06)
Features contain minimal predictive signal for soil moisture
Non-linear models show marginal improvement over linear
RMSE ≈ baseline (predicting mean) for all models

## Slide 20
Why Prediction Failed
Missing critical variables (rainfall, temperature, soil type)
Spatial-temporal misalignment between sensors
Radar signals confounded by surface roughness and vegetation

## Slide 21
Conclusion
Complete ML pipeline successfully developed and evaluated
SVR-RBF and Neural Network achieved best performance (R² ≈ 0.05)
Radar backscatter alone insufficient for accurate prediction
Transparent reporting of negative results has scientific value

## Slide 22
Future Scope
Integrate meteorological data (rainfall, temperature)
Add soil property maps and vegetation indices (NDVI)
Implement time-series models (LSTM) for temporal dynamics
Physics-informed ML incorporating domain knowledge

## Slide 23
Thank You!
Questions & Discussion
Sachin Dimri
Machine Learning Project | February 2026